Troubleshooting for electromagnetic clutch fan

The operating principle of the fan is that, when the water temperature reaches over 82 degrees, the rotating speed of the fan is synchronous with rotating speed of the engine crankshaft. By examining the power supply to the two-hole plug-in connector mounted on the engine, it is possible to check if the electronmagnetic clutch fan works properly (the prerequisite condition is that the default fan is in good condition)

1.	For O’long trucks (S2000), check if the black green wire of the two-hole plug-in connector is live and the brown wire is grounded. If the black green wire is live and the brown wire is grounded, it will be considered that the electromagnetic clutch fan works properly. If the air conditioner is available and the engine is working, turn on the air conditioner. If the red wire of the single-hole plug-in connector is live, the rotating speed of the fan should increase correspondingly.

2.	For D’long trucks(F2000, F3000), check if the white wire (15001) of the two-hole plug-in connector is live and the brown wire is grounded, it will be considered that the electromagnetic clutch fan works properly. If the vehicle is equipped with air conditioner, when the engine is started, switch on the air conditioner, the white wire (23300) of the single-hole plug-in connector will be live, and the rotating speed of the fan should increase correspondingly. Both the connector of the wire harness of the electromagnetic clutch fan in the cab and the wire harness on the chassis can be match and are three-hole plug-in connector X03, on which wire 23300 is connected to the electromagnetic switch relay of the compressor K146, wire 15001 to the terminal No. 94 on the central electrical panel A100, and wire 31000 to the right earth point X the cab.

# Text boxes

Check if the brown wire is earth connected

Check if the black green wire is charged with electricity

Temperature control module of the engine

Temperature control module power of the engine 2-hole connector

Safe of power supply

Temperature control module of the engine

Output of electronic controlled fan of the engine

Single-hole plug-in connector of work signal input of the air conditioner

Check if the white wire is charged with electricity

Check if the brown wire is earth connected